## Slide 1: Accelerated Open Source vBRAS Solution Based on OpenBRAS and VPP/DPDK
Hongjun Ni & Liang Ou, Yujia Luo
Intel China Telecom
Acknowledgement:
Heqing Zhu, John DiGiglio, Beilei Xing @Intel
Neale Ranns @Cisco

## Slide 2
Agenda
  BRAS in China Telecom
  OpenBRAS Architecture
  vBRAS Deployment
  Data Plane implementation
  Distribute traffic using NIC
  Key Takeaway

## Slide 3
Biggest IP backbone in the world
Chinanet (100 million BroadBand subscribers)
IP Backbone for Internet Service
150 cluster routers，2000 link
MAN interconnect，traffic aggregation
300 MANs，Capacity over 30T
Over 10K BRAS hardware devices
BRAS in China Telecom
IP Network of China Telecom
What is BRAS？Broadband Remote Access Server
  authenticate, authorize and route broadband subscriber data traffic according to customized policies
MAN
Enterprise
Chinanet
MAN
MAN
ITSupport
System
AAA
V
-
NET
IDC
PC
PC
IPTV
PC
BRAS
SR
SR
BRAS
BRAS
Enterprise
Internet
CR
Where does BRAS locate ?
Notes: Hello, everyone, I’m Yujia LUO from China Telecom. It’s my honor to share something about our open source vbras based on vpp.
First let me introduce BRAS, which is short for broadband remote access server. Basically it’s a network device used to authenticate, authorize and route subscribers’ data traffic.
The location of bras can be found in this picture, between the access network and metropolitan network, where we called central office. There are over 10 thousand bras in China telecom network and we hold the most biggest IP backbone in the world.

## Slide 4
Traditional BRAS Architecture
Drawbacks:
1. Control Plane and Forwarding Plane are tightly coupled
2. Not flexible to scale
IP address
Mgnt
User
Mgnt
Routing
(BGP/IGP)
Radius
Session Mgnt
Forwarding Engine
DHCP
Server
Radius Server
BRAS
PPPoE
IPOE/DHCP
PPP
TCP/IP
BRAS
=
Router
Access Management
+
Notes: Before NFV is introduced, the traditional bras is a hardware device that merge router and access management functions together.
But the drawbacks are quite obvious. The control plane and forwarding plane are tightly coupled, which makes it slow or difficult to do any single change. It’s not efficient and inconvenient.

## Slide 5
Legend
Control plane
Data plane
OpenBRAS Control Plane
MANO
OpenBRAS Data Plane
NFV-O
GVNFM
Cloud Management
OpenStack
Kubernetes
vDHCP
v
vAAA
Session discovery service
PPPoE
PPP
IPoE
Southbound
Plugins
RESTCONF
Openflow
NETCONF
Microservice Bus
Classifier
ACL
Policer
Routing
Decap
Uplink
ACL
Encap
HQoS
Routing
Downlink
Slow Path
Control Plane Agent
L2TP
Data plane control service
Subscriber
ACL
QoS
Routing
Common service
ACE
libevent
DPDK
VPP
Commercial Software
SmartNIC
Socket
vBRAS Architecture
www.openbras.org.cn
vBRAS based on rack
Supported Data Plane Options
Notes: So NFV try to solve the problem by seperating the software from hardware.
BRAS is virtualized into an app which is called vbras and is installed on servers.
What is more, the router function and access management function of bras are seperated too.
The access management function becomes control plane, and Router becomes data plane.
The control plane includes session discovery service, data plane control service, common service and southbound plugins. China Telecom uses PPPoE or IPoE protocol during session discovery process.
The data plane supports various options like VPP, DPDK, smart nic and so on to accelerate the forwarding process.
This architecture of vbras actually comes from the OpenBRAS project, which is an open source project founded by china telecom, intel, inspur, mellanox and many other partners. I will talk about this later.

## Slide 6
PPPoE/IPoE Processing of vBRAS
OpenBRAS Control Plane
VxLAN
VPP
Port0
Session Table
Dst IP address | Action
Forwarding table
Access Port
Uplink Port
IP forwarding
Port1
User MAC | Session ID | User IP address | Access Protocol
VPP-Classifier
Session discovery service
PPPoE
PPP
IPoE
RESTCONF
Openflow
NETCONF
L2TP
Data plane control service
Subscriber
ACL
QoS
Routing
Southbound
Plugins
OpenBRAS Data Plane
PPPoE/IPoE
NETCONF
Notes: This page shows a specific case we’d like to share. We utilized vpp to realize the offloading of PPPoE/IPoE processing.
Previously, all the flow will be sent to control plane which keeps CPU very busy. May jobs have to stay inline and wait for CPU, which is slow.
So we decided to move some of the jobs from control plane to data plane. After offloading, VPP can help to classify the flow, and some of the flow can be forwarded to uplink port directly.

## Slide 7
What does VPP need to do?
Identify PPPoE Discovery and Session packets
  With eth_type 0x8863 and 0x8864
Identify PPP Packets with ppp_protocol 0x0021
  Which are identified as IP packets
Identify DHCP Packets with (udp_src_port, udp_dst_port) = (67, 68) or (68, 67)
Identify Routing Packets (BGP/IGP)
Encap or Decap PPPoE and PPP packet
  Forward packets between access port and uplink port
Look up table
  Session table to determine whether the traffic is allowed to forward
  Forwarding table to determine which port to forward the traffic
Notes: Here is what VPP needs to do. Basically there are 3 kinds of jobs.
The first one is to identify packets, some of the packets are directed to the control plane, and some are forwarded directly.
The second is to encapsulate and decapsulate the packet.
The last thing is to look up the tables. There are 2 kinds of table.
Session table determines whether the flow is legal or not.
Forwarding table determines which port to forward the traffic.

## Slide 8
vBRAS Processing Flow and Pseudo Code
Notes: This page shows the detail logic of vbras processing, which I’m not going deep into it.

## Slide 9
Orchestration
Layer
Network Control
Layer
Infrastructure
Layer
Where does vBRAS locate in China Telecom ?
vBRAS
NFVI
IP
Optical
2G/3G
4G
5G
IP Metro
Controller
Transport
Controller
SDN Controller
VIM
VNFM
EMS/NMS
SDN-O
SDN/NFV Network Orchestrator
NFV-O
Pub App
Ents App
3rd App
OSS/BSS
API
API
Open API
DC
Ctrl
PIM
Access
vIMS
NFVI
GS-O
Access
Controller
NFVI ctrl
Edge Cloud
Core Cloud
Notes: When talking about the deployment of vbras, we all agree that vBRAS should be put in NFV environment together with VIM, VNFM, controller and orchectrator.
This is a big move from our traditional architecture, and many work have to be done. The industry had already paid attention on this area, and the most famous case is the CORD project. I think everybody knows that.
China telecom shares the same idea. We are trying to re-architect the old framework. In case of the infrastructure layer, we plan to divide it into 2 parts, the edge cloud and the core cloud, and vBRAS mainly located in edge cloud.

## Slide 10
Possible Deployment of vBRAS
vBRAS-UP
Traditional
BRAS
CR
vBRAS-UP
PON
PON
vBRAS-CP
vBRAS-CP
Internet
Subscriber
Subscriber
PPPoE/IPoE
IPTV
VoIP
Core Cloud
Edge Cloud
ITMS
Notes: We believe that the traditional bras and vbras will coexist for a very long time.
The possible deployment solution of vbras is shown in the picture. The data plane locates in edge cloud because it’s close to the user. The location of control plane varies according to the service.
For example, service like IPTV and surfing the Internet create tremendous traffic flow, so we suggest the control plane should be located in the same cloud as the data plane. But for service like VoIP and ITMS, the control plane could be centralized in core cloud.

## Slide 11
OpenBRAS Promotes vBRAS Deployment
China Telecom vBRAS Technical white Paper
Include industry trends, key elements, use cases, and solutions of vBRAS
vBRAS offloading Solution
vBRAS offloading solution based on Smart NIC
Smart NIC: jobs like PPPoE/PPP En/Decap, traffic forwarding
vBRAS CO Deployment Reference Solution
Redesign CO based on NFVI, considering room area, floor bearing, power supply, cooling system
Provide some typical device specifications
Project: Dedicated to build an open source vBRAS system, providing reference design
www.openbras.org.cn
Notes: As I mentioned before, openBRAS is a project aiming at promoting vBRAS deployment.
It is dedicated to build an open source vBRAS system and to provide reference design.
Developers will find white papers, solutions, source codes of reference design and tools on our official site.
Last year, we published China Telecom vBRAS Technical White Paper, which includes industry trends, key points of vBRAS, use cases, and solutions.
In order to enhance the performance of vBRAS data plane, we presented vBRAS offloading solution based on vpp and smart nic.
In addtion, China Telecom also focus on NFV infrastructure of Central office. We had done a lot of NFV decoupling test and met some problems. Form of hardware varies, and there is no unified way to configure and obtain the information.
The process of deploying, installing, integrating are repeated and error-prone.
What’s more, conditions like room area, floor bearing, power supply, cooling system are not always satisfying.
So together with our partners, we came up with the solution of all-in-one delivery, which can be found on our website too.

## Slide 12
Upstream Processing
VPP-based BRAS
Upstream Worker 0 - N
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
NIC
NIC
Downstream Worker 0 - N
ETH
PPPoE
IP
ETH
IP
OpenBRAS
(PPPoE/PPP handshaking)
Tap port
Dataplane
Control Plane
PPPoE
PPP
DHCP
Radius
PPPoE Plugin
-DP/CP dispatch, PPPoE decap
Policer -Mark & Pass
IP-Lookup -route packet
DPDK Input
Eth Input
IP-Rewrite –add Eth Hdr
Intf Out
-DPDK Tx
ACL
RSS Acceleration with FVL DDP
PPPoE Plugin
-DP/CP dispatch, PPPoE decap
Policer -Mark & Pass
IP-Lookup -route packet
DPDK Input
Eth Input
IP-Rewrite –add Eth Hdr
Intf Out
-DPDK Tx
ACL
PPPoE Plugin
-DP/CP dispatch, PPPoE decap
Policer 0 -Mark & Pass
IP-Lookup -route packet
DPDK Input
Eth Input
IP-Rewrite –add Eth Hdr
Intf Out
-DPDK Tx
ACL

## Slide 13
Downstream Processing
VPP-based BRAS
Downstream Worker 0 -N
HQOS
NIC
Upstream Worker 0 - N
ETH
IP
ETH
PPPoE
IP
NIC
Intf Out
-DPDK Tx
Port x 1 :: 25Gb
SubPort x 1 :: 25Gb
Pipe x 4096 :: 6.1Mb
TC x 4 :: 6.1Mb
DPDK Input
IPv4 Input
IPv4 Lookup -route packet
IPv4 Rewrite
-PPPoE encap
-Add Eth Hdr
RSS Acceleration with FVL DDP
DPDK Input
IPv4 Input
IPv4 Lookup -route packet
IPv4 Rewrite
-PPPoE encap
-Add Eth Hdr
DPDK Input
IPv4 Input
IPv4 Lookup -route packet
IPv4 Rewrite
-PPPoE encap
-Add Eth Hdr
.
.
.
.
.
.
.
.
.

## Slide 14
Distribute traffic on NIC
Upstream Traffic
Downstream Traffic

## Slide 15
Distrute traffic evenly
Test setup:
64K PPPoE sessions
4 cores for upstream
4 cores for downstream

## Slide 16
PPPoE Plugin - Discovery and Session Setup
Dispatch packets between client and OpenBRAS.
Learn PPPoE FIB.
Create PPPoE session.
Create downstream route entry automatically.

## Slide 17
PPPoE Plugin – Upstream and Downstream

## Slide 18
ACL and Policer
ACL:
One ACL rule for each subscriber.
Configurable to match any field.
Policer:
One policer rule for each subscriber.
Configurable to match any field.
Actions: conform/exceed/violate.

## Slide 19
Hierarchical Qos (HQos based on DPDK) added to VPP
Level | Siblings per Parent | Description
Port | . | Output Ethernet port 1/10/40 GbE.
Subport | Configurable (default: 8) | A predefined group of users
Pipe | Configurable (default: 4K) | An individual user/subscriber
Traffic Class (TC) | 4 | A different traffic type with specific loss rate, delay and jitter.
Queue | 4 | Hosts packets from multiple connection of the same type belonging to the same user

## Slide 20: Key Takeaway
A solution with separated Control Plane and Data Plane.
Implementation ready for Cloud Edge deployment.
Control Plane leverages OpenBRAS, an open source project.
Data Plane leverages VPP and DPDK.
Distribute traffic from NIC to multiple cores evenly.
http://fd.io/